## Slide 1
Session 9: Introduction to Global Navigation Satellite System (GNSS)
Introduction to geospatial data management
and technologies for Health Programs training workshop - Timor Leste

## Slide 2
Constellation of satellites providing signals from space that transmit positioning and timing data to GNSS receivers. The receivers then use this data to determine its location.
Global Navigation Satellite System (GNSS)
2

## Slide 3
There are currently four different satellite navigation systems providing autonomous geospatial positioning:
GPS (USA), GLONASS (Russia), BeiDou (China), and Galileo (EU).
3
Global Navigation Satellite Systems (GNSS)

## Slide 4
1. Satellite unique identifier
2. Almanac data (state and orbital information to calculate which satellites are visible)
3. Ephemeris data (precise orbital information to calculate satellite location)
No need for internet!!!
4
GNSS – How it works
The signal received from each satellite contains:

## Slide 5
?
?
?
?
?
?
?
When receiving the signal from only one satellite
5
GNSS – How it works
1
Satellite 1: 17,000 km
The device can be anywhere of a sphere with a radius equal to the distance measured between the satellite and the device

## Slide 6
?
?
?
?
?
?
?
?
6
GNSS – How it works
When receiving the signal from only two satellites
Satellite 1: 17,000 km
Satellite 2: 20,000 km
The device can be anywhere along the circle generated by the intersection of the sphere of each satellite

## Slide 7
Reason why you need at least 4 satellite signals to get a good reading
As soon as you receive the signal from 3 satellites...
…and with 4 signals
Facilitated by the existence of the 4 constellations (if your device can receive their signal)
7
GNSS – How it works
Intersection between the circle and one more sphere => 2 points
Only 1 point possible

## Slide 8
Good PDOP
Positional Dilution of Precision (PDOP)
Another challenge addressed by the existence of the 4 constellations
GNSS - Source of signal errors
8
Poor PDOP
It is preferable to have a good dispersion and to look at the accuracy measurement given by the device

## Slide 9
Natural and artificial barriers
Important to be in the most open space possible when collecting geographic coordinates
9
GNSS - Source of signal errors

## Slide 10
Signal multipath
1
2
1
2
10
Important to be in the most open space possible when collecting geographic coordinates
GNSS - Source of signal errors

## Slide 11
Minimum requirements:
1. Allows to be configured as follows:
  a. Position format (decimal degrees: hddd.ddddd)
  b. Map datum/Cartographic reference system: WGS84
  c. Map spheroid: WGS84
  d. Distance and speed: Meter
2. Provide a reading with at least 5 decimal places to reach a level of precision down to the meter
3. Display the following information:
  a. Number of satellite signals received
  b. Accuracy measure
4. Having access to GPS and GLONASS constellations (Also having access to Galileo and Bei Dou is a big plus)
Large selection / different prices!
11
GNSS - Devices
A smart phone with a good GNSS receiver and an app is the option being used the most frequently nowadays

## Slide 12
Android
GPS Essentials is a free app available for Android devices with a built-in GNSS receiver that complies with all the recommended requirements
GNSS Apps for smart phones (Android, iPhone)
12
iOS Phone
“My GPS coordinates” is a free app available for Apple devices (iPhone/iPad)
These app can be used as an alternative to dedicated GNSS-enabled devices when collecting geographic coordinates as the combination complies with the specifications mentioned in the previous slide
Notes: Android devices and GPS Essentials
As mentioned earlier, there are smart phones, particularly Android-based devices, that have built-in GNSS receiver.
One mobile app that can be used on these Android-based devices is the GPS Essentials.
You will be using GPS Essentials to complete Exercise 4.A

## Slide 13
Must match the data specifications
Taking a reading
GPS and GLONASS activated
Accuracy value
Number of satellite signals received
Coordinates
GNSS device
Mobile phone + app
Position of
satellite
GNSS - Unit setting
13

## Slide 14
Easiest georeferencing method to use
  Standardized, stable, unique, infinitely fine resolution
Uses a well-defined and fixed frame of reference
  Based on the Greenwich (Prime) Meridian and the Equator
Most used in geospatial technologies
  Can be easily projected if needed
GNSS - Why using decimal degrees (latitude and longitude)?
14

## Slide 15
Recommended
15 m
GNSS - Scale, accuracy and precision
15

## Slide 16
With GNSS-enabled device
Without GNSS-enabled device
GNSS - Data collection methods
16
https://www.healthgeolab.net/DOCUMENTS/Guide_HGLC_Part2_4_2.pdf

## Slide 17
Description of the device being used
Device and/or app user manual (buttons, functions, etc.)
How to configure the device and/or app
Material to use in addition to the device and/or app (e.g. form, other documents)
Step-by-step process for data collectors
It is important to have and follow a Standard Operating Procedure (SOP)
GNSS - Standard Operating Procedure (SOP)
17
The SOP should at least cover:
https://www.healthgeolab.net/DOCUMENTS/Guide_HGLC_Part2_4_2.pdf
It is also important to have an SOP for the supervisors

## Slide 18
This phase is critical for the data collectors to be independent in the field and able to collect high quality geographic coordinates with minimal supervision
GNSS – Before data collection
18
Two primary actions:
Prepare the material needed to implement the selected data collection method
Select and train the data collectors and their supervisor(s)

## Slide 19
GNSS – Before data collection (material preparation)
19
The preparation of the material must cover the:
Selection of the collection method that will be implemented
Adjustment of the data collection form to match the selected method
Creation of the electronic form, if required
Preparation of the associated documents and material
Development of the SOP to be implemented in the field
Installation of the applications on the devices if required
Configuration of the devices and/or app and verification that the GNSS receiver is working correctly
Preparation of the training material
GNSS receiver working correctly
Potential issues with the GNSS receiver
Landmark visible on satellite images
Device
readings

## Slide 20
GNSS – Before data collection (selection and training of collectors)
20
Knowledge and experience in using GNSS-enabled devices should be considered when selecting data collectors and their supervisor(s).
In addition to selecting qualified data collectors, training data collectors and their supervisor(s) is one of the, if not the most, important steps in the pre-survey process.
This is what will make the difference between…
…this… ..and this

## Slide 21
GNSS – Before data collection (training)
21
The training should aim to provide a good understanding of the concepts and process behind the collect of accurate geographic coordinates, the data collection equipment, and the SOPs. The training should also cover appropriate troubleshooting methods regarding commonly encountered issues while in the field
To achieve these goals, the training should at least cover the following topics:
Overview of existing GNSS and use of the chosen GNSS-enabled device
Introduction to the GNSS-enabled device
SOP to complete the data collection instrument
Hands-on practice session
It is important to:
Allocate enough time for the above-mentioned session.
Ensure that the participants can ask questions.
Give copies of the different documents to all the participants.
Ensure every participant has the opportunity for hands-on practice of using a GNSS-enabled device.
Check all the GNSS-enabled devices to be used in the field if not already done

## Slide 22
GNSS – During data collection
22
During the field data collection exercise, the data collectors should follow the SOP using the associated documents that have been provided to them.
Despite a high-quality training session, it remains important to verify the methods used to collect the geographic location information and address any unexpected issues while the data collectors are in the field.
The following verification steps should be followed depending on available resources and the extent of the surveyed area:
On-site spot checks of data accuracy and completeness conducted by the data collection supervisor. Part of the check for accuracy can be performed using Survey123 for ArcGIS, Maps.Me, or Google Maps as way to ensure that the point is falling in the expected area.
Verification of the data remotely through periodic submissions of the collected data in a spreadsheet, either using Google Sheets online or emailing a Microsoft Excel spreadsheet to the data collection supervisor. For certain applications, a purpose-designed online database system may be used as well. However, these solutions usually require a regular access to the internet.

## Slide 23
GNSS – After data collection
23
Ensure that the collected data is organized in a structured table that can be saved as a spreadsheet (e.g. in Microsoft Excel) and should contain all the fields that are on the data collection form
Don’t forget about the data catalogue and metadata worksheets

## Slide 24
Choose the appropriate GNSS-enabled device (check the quality of the GNSS receiver) and data collection method
Use a pre-established Standard Operating Procedure (SOP) which includes all the necessary information for the data collectors to properly collect coordinates in the field (e.g. source of error signals) as well as a SOP for the supervisors
Collect high accuracy (instrumental accuracy below 15 meters) and high precision (5 digits after the decimal point) coordinates
Invest in a good training for data collectors and supervisors
Establish a good monitoring process during data collection
Properly store and document the geographic coordinates resulting from the data collection exercise
Note: Pay attention to potential ethical issues when locating or tracking individuals with a high accuracy !!!
GNSS - Summary
24